Cold Comfort:
Cold Temp Restricted Airports
Pilot requirement at certain airports, not assigned by ATC
Unrelated to Baro-VNAV temperature restrictions
“High-to-low, look out below” due to density
Procedure and table in AIM Chapter 7-3
Approaches only, not MIA or MVA, but you can request higher for safety

---
Starting Point: The Chart
- Need to check for snowflake restriction in “notes box”
- Active when reported surface temperature is at or below limit
- Example we’ll use at right is KBTV RNAV Z RWY 33

---
Step Two: Affected Segments
Optional: find segments affected in Cold Temperature Airports document
https://aeronav.faa.gov/d-tpp/Cold_Temp_Airports.pdf
- KBTV above is intermediate segment only; can be initial, intermediate, final, or missed.
- At pilot’s option, may modify all segments.

---
Segment Details
- For initial and intermediate segment, use FAF altitude and adjust all altitudes from IAF leading up to (and including) FAF.
- For final segment, use MDA or DA and adjust all fixes past FAF.
- For missed segment, use final missed altitude and adjust that one only.

---
Step Three: Compute Adjustments
- Find height above ground (FAF 3800 – 335 elevation = 3465)
- Look up in ICAO Doc 8168 or AIM 7-3-5
- If it's -20C, compute 495’ from the table, round up to 500’, and add that to intermediate and FAF altitudes

---
Initial and Intermediate Adjustment Results
3800+500=4300, 4800+500=5300, 5400+500=5900, 6000+500=6500

---
Repeat: Final and Missed
- Select minimum. LPV is 584’, 584-335=249. Add 40’ from chart, so new minimum is 624’.
- Missed is 3000’. 3000-335=2665. Via chart, 300’ correction. New missed altitude is 3300’.

---
Step Four: Notify ATC
- If initial, intermediate, or missed are adjusted, must notify ATC
- No ATC notification for adjustments to final segment, either for step-downs or for minimums
- Phrasing: “Require 4300 feet until EHIKO for cold temperature operations”
- ATC cannot refuse this request

---
Final Thoughts
- You'll want to compute these things ahead of time, because it's complicated and not supported by ForeFlight or other EFBs
- Doesn't affect your ability to get in when weather is low; actual altitude is the same
- Only airports with a runway greater than 2500' evaluated; others at pilot discretion
- Doesn't affect glide slope but can change DA
- Garmin V6.50 on 750/650 can compute it in some installations; see AFM